## Slide 1: R&E Aduino Programming
Hyung-Seok Park
Information and Communication Engineering
DGIST
http://csi.dgist.ac.kr
hyungseok@dgist.ac.kr

## Slide 2
Install Library
LCD 1602 with I2C
  LiquidCrystal (by Adafruit)
Contractless Infrared Temperature Sensor
  Adafruit MLX90614 Library (by Adafruit)
DHT22
  DHT sensor Library (by Adafruit)
  Adafruit Unified Sensor (by Adafruit)
IR remote
  IRremote (by shirriff)

## Slide 3
Programming
Contractless Infrared Temperature Sensor
#include <Adafruit_MLX90614.h>
Adafruit_MLX90614 mlx = Adafruit_MLX90614();
void setup() {
mlx.begin();
}
void loop() {
String strTemp = String("");
strTemp += (double)(mlx.readObjectTempC());
lcd.setCursor(0,1);
lcd.print(" ");
lcd.setCursor(0,1);
lcd.print(strTemp);
}

## Slide 4
Programming
DHT22
#include <DHT.h>
DHT dht(2, DHT22);
void setup() {
dht.begin();
}
void loop() {
int dht_h = dht.readHumidity();
int dht_t = dht.readTemperature();
lcd.setCursor(7,1);
lcd.print(dht_h);
lcd.setCursor(10,1);
lcd.print(dht_t);
}

## Slide 5
Programming
Pulse Sensor
int PulseSensorPurplePin = 2;
int HeartSignal;
int Threshold = 425;
int buffer[1000] = {0};
int idx = 0;
int BPM = 0;
void loop() {
HeartSignal = analogRead(PulseSensorPurplePin);
if (buffer[idx] == 0 && buffer[((idx+1)%1000)] == 1) BPM--;
if (HeartSignal > Threshold) {
buffer[idx] = 1;
} else {
buffer[idx] = 0;
}
if (buffer[((idx-1)%1000)] == 0 && buffer[idx] == 1) BPM++;
idx = (idx + 1) % 1000;
// Serial.println(HeartSignal);
lcd.setCursor(13,1);
lcd.print(BPM);
}

## Slide 6
Programming
Serial Print
void loop() {
Serial.print(strTemp);
Serial.print(", ");
Serial.print(dht_h);
Serial.print(", ");
Serial.print(dht_t);
Serial.print(", ");
Serial.print(BPM);
Serial.print(", ");
Serial.println(setTemp);
}